## Slide 1: Modern Processors & Parallel Computing
Zhenbang You
2022/11/02

## Slide 2: My Background
2018-2022
Bachelor of Science in Computer Science and Technology
2022-
Master of Science in Computer Science
Systems Track

## Slide 3
“It is not a dreary science of paper machines that will never work. No! It’s a discipline of keen intellectual interest, requiring the balance of marketplace forces to cost-performance-power, leading to glorious failures and some notable successes.”
J. Hennessy, D. Patterson, Computer Architecture: A Quantitative Approach

## Slide 4: Outline
Parallelism and programming model (from the perspective of implementation)
  Instruction-Level Parallelism (ILP)
  Data-Level Parallelism (DLP)
  Thread-Level Parallelism (TLP)
  Parallelism can also be categorized from a logical perspective
    We will talk about this later
Performance of programming languages

## Slide 5: Characteristics of the Lecture
Separation of abstraction and implementation
  Try to give you clean programming models
Considering processors and memory at the same time
  Performance = parallelism + locality

## Slide 6: Before We Start
What is the source of parallelism?
  Lack of dependencies!!!
  We will keep realizing this in the lecture

## Slide 7: Instruction-Level Parallelism (ILP)
Start from PIPE you learned in CSAPP
Why pipelining?
  Why is it possible to do pipelining?
  What are its advantages and disadvantages?
  What is the next step to improve PIPE?

## Slide 8: Instruction-Level Parallelism (ILP)
Start from PIPE you learned in CSAPP
Why pipelining?
  Why is it possible to do pipelining?
    The lack of dependencies among instructions
    But dependencies still exist sometimes, thus we need forwarding and stall/bubble
  What are its advantages and disadvantages?
    More transistors for better performance
      Complex, thus error-prone and expensive
  What is the next step to improve PIPE?
    A large number of books answering this question
    One of the leading force that drove the improvement of processors in at least three decades

## Slide 9: Instruction-Level Parallelism (ILP)
Instructions/sec = instructions/clock (IPC) * clocks/sec (frequency)
In the ILP-dominant era, the performance improvement mainly come from three kinds of force

## Slide 11: Instruction-Level Parallelism (ILP)
Instructions/sec = instructions/clock (IPC) * clocks/sec (frequency)
In the ILP-dominant era, the performance improvement mainly come from three kinds of force
  Semiconductor manufacture technology
    The latest: TSMC 5nm process
  Hardware design
  Compilers
    Key takeaway: ILP is done by both hardware and compilers

## Slide 12: Instruction-Level Parallelism (ILP)
What do programmers need to do?

## Slide 13: Instruction-Level Parallelism (ILP)
What do programmers need to do?
  Buy new hardware
    “The more you buy, the more you safe.” ---- Jensen Huang
  Install the latest compiler
  Free ride!
    Yes, it was the case.
    But it ended in 2005

## Slide 14: Instruction-Level Parallelism (ILP)
A little bit about implementation
  Directed acyclic graph (DAG)
  Vertex: one stage of an instruction
  Edge: dependency between vertices
Example
  Pipelining, deeper pipeline (more vertices, less dependencies)
  Superscalar execution, multiple issue
  Out-of-order execution (dynamic scheduling, hardware) & instruction scheduling (static scheduling, compiler)
  Register renaming
  Branch prediction

## Slide 15: Limitations of ILP
Three walls
  Memory wall
    Latency is the key bottleneck
      Latency vs bandwidth
  Power wall
    Especially for low-end devices and devices emphasizing power-efficiency
  ILP wall
    Potential ILP it limited

## Slide 16: Data-Level Parallelism (DLP)
Programming model/data-parallel thinking
  Vectorization/Single Instruction Multiple Data (SIMD)
    Organize computation as operations on vectors
    Example
      PyTorch:

## Slide 17: Data-Level Parallelism (DLP)
Another example
  Scala
    Functional programming: map, reduce
    Compared to PyTorch:
      “c = a + b” corresponds to “map” (element-wise operation)
        Can be done in constant time given enough processors
      “d = a.sum()” corresponds to “reduce” (reducing a vector into a scalar)
        Can be done in logarithmic time given enough processors
    Scales to distributed systems (beyond a single machine)
      Simple as it seems, it is indeed extremely powerful!
      We will see other programming platforms for DLP share the same programming model

## Slide 18: Data-Level Parallelism (DLP)
Example: x86 AVX intrinsics
  Platform-dependent
  Add (map operation)
  __m256 contains float * 8

## Slide 19: Data-Level Parallelism (DLP)
Example: x86 AVX intrinsics
  Sum (reduce operation)
  Ignoring non-associativity of float

## Slide 20: Data-Level Parallelism (DLP)
Where does the potential of DLP comes?
  ILP: lack of dependencies among instructions
  DLP: lack of dependencies among (____)

## Slide 21: Data-Level Parallelism (DLP)
Where does the potential of DLP comes?
  ILP: lack of dependencies among instructions
  DLP: lack of dependencies among elements

## Slide 22: Data-Level Parallelism (DLP)
Implementation (three categories)
  Common feature: one instruction operates on multiple data
  CPU (requires extra hardware units)
    Deeper
      More pipeline stages to achieve higher frequency
      Vector architecture
        E.g., RISC-V vector extension, ARM Neon
        Reviving!
    Wider
      Wider registers, wider ALU, …
      Multimedia SIMD extension
        E.g., AVX (AVX/AVX allows 32bit*8 or 64bit*4)
    Programmed by intrinsics, platform-dependent but largely the same

## Slide 23: Data-Level Parallelism (DLP)
Implementation (three categories)
  CPU
    Disadvantages
      Power-hungry
        AVX512 is extremely power hungry
        Static power is always there no matter whether you use it
        Intel efficient cores (little cores) do not support AVX512
      Transistor count
      Costly for context switch
        In real systems, you need to save/restore registers on a routinely basis
        You will learn this in chap 8
      Vector architecture is much more complex than AVX

## Slide 24: Data-Level Parallelism (DLP)
Implementation
  GPU
    Usage
      Graphics
      Scientific computing
      Deep learning
      Cryptocurrency mining
    Multiple SIMD processors
      Very simple pipeline
      Low frequency (1-2.5GHz vs 3-6GHz of CPU)
      Each core is much less powerful than that of CPU
      But GPU has lots of cores!
        AMD 5990X: 64 cores, NVIDIA 4090: 16384 cores
    Programmed by CUDA (NVIDIA) and OpenCL (others)

## Slide 25: Data-Level Parallelism (DLP)
GPU
  Requirements for memory
    Bandwidth instead of latency
    GDDR, HBM
      GDDR vs DDR
      Bandwidth vs latency
      HBM: the future, high bandwidth, low latency, still expensive

## Slide 26: Data-Level Parallelism (DLP)
Memory bandwidth comparison
  Typical PC CPU
    DDR4-3200, 2 channels: 3200 MHz * 8 B * 2 channels = 51.2 GB/s
    DDR5-4800, 2 channels: 4800 MHz * 8 B * 2 channels = 76.8 GB/s
  Extremal server CPU
    DDR5-6400, 8 channels: 6400 MHz * 8 B * 8 channels = 409.6 GB/s
      Beyond current technologies
  PC GPU
    NVIDIA 4090: 1,008GB/s
    NVIDIA 3060: 360GB/s
  Enterprise-level GPU
    NVIDIA H100 SXM5: 1,920 GB/s
  Apple M-series
    M1 Max: 400 GB/s
Memory bandwidth can sometimes be one of the key factors contributing to the huge performance gap between CPU and GPU

## Slide 27: Data-Level Parallelism (DLP)
GPU
  Disadvantages
    Transferring data between main memory and VRAM (GPU memory): high latency, low bandwidth

## Slide 28: Data-Level Parallelism (DLP)
Most scalable
Most efficient
  Cost-efficient, power-efficient
    Cost-power-performance
  As long as you have enough DLP

## Slide 29: Thread-Level Parallelism (TLP)
2005: the advent of multi-core CPU
  Sun UltraSPARC T1
    4/6/8 cores, 4 threads/core
    The first practical multicore processor
    One of my instructors of CS149, Kunle Olukotun, was one of its architects
  AMD Athlon 64 X2
    2 cores
Lack of dependencies among what?

## Slide 30: Thread-Level Parallelism (TLP)
2005: the advent of multi-core CPU
  Sun UltraSPARC T1
    4/6/8 cores, 4 threads/core
    The first practical multicore processor
    One of my instructors of CS149, Kunle Olukotun, was one of its architects
  AMD Athlon 64 X2
    2 cores
Lack of dependencies among what?
  Tasks!

## Slide 31: Thread-Level Parallelism (TLP)
Multiple Instructions Multiple Data (MIMD)
  MIMD vs SIMD
    Flexibility
      Task parallel vs data parallel
        Two kinds of logical parallelism that application programmers care about
      Heterogenous vs homogenous
    Efficiency
    Scalability

## Slide 32: Thread-Level Parallelism (TLP)
C++20: std::jthread
Fork-join
  Sum can be implemented in the same style. Try it yourself.
  You will find how hard it is to program in pthread two months later

## Slide 33: Thread-Level Parallelism (TLP)
You will learn how to programming multiple threads in Chapter 12
  But the programming interfaces introduced in CSAPP are hard to use
  Recommend:
    C++: std:: thread, std::jthread, std::future
    Java: thread, future
    Go: goroutine
    Scala/Haskell: Future

## Slide 34: Thread-Level Parallelism (TLP)
Multiple cores
  Cache
    Cache coherence & memory consistency
      No plan to talk about this in the lecture
Multithreading
Heterogeneous cores
  E.g., ARM big-LITTLE, intel performance cores & efficient cores

## Slide 35: Thread-Level Parallelism (TLP)
Less larger cores vs more smaller cores
  Varying among different scenarios
    For PC gamers, prefer less larger cores
    For cloud service provider, prefer more smaller cores
      AMD c series, e.g., ZEN4c, 128 small cores
      AWS designs its own processors to achieve better power efficiency

## Slide 36: Thread-Level Parallelism (TLP)
Limitations
  Scalability
    Why don’t we have more cores?
      Communication
      Coherence
      Yield
        Chiplet
      Amdahl’s Law
        How much you can improve depends on how much you can’t improve
        There is always code that can’t be parallelized

## Slide 37: Thread-Level Parallelism (TLP)
Memory requirements
  Latency: ILP > TLP > DLP
  Bandwidth: DLP > TLP > ILP

## Slide 38: The era of cloud computing
If we can assemble computation from the crowd, there may be more parallelism we can use
  This is called Request-Level Parallelism (RLP)
  Loosely coupled task parallelism
This is the key argument of cloud computing
Very hot topic, both in the industry and in the academia

## Slide 39: Computation hierarchy
Computation hierarchy
  Core -> processor > cluster
  ILP -> DLP -> TLP -> RLP
Memory hierarchy
  Register -> per-core cache -> shared cache -> memory -> disk -> remote storage

## Slide 40: The Era of Domain-Specific Architecture (DSA)
DSA typically exploits different kinds of parallelisms in certain scenarios
Wait, this should require lots of domain-specific languages (DSL)!
But there aren’t too many kinds of parallelisms and programming models
  Personally speaking, I think it’s the key to why DSA may make a difference in the future
  Compilers play a key role
CPU and GPU only occupy 1/3 die size in your smartphone processor
Very hot topic in the academia, but its industrial potential is still to be seen

## Slide 41: Performance of Programming Languages
A few words before starting
  The performance of a program highly depends on code quality, and thus highly depends on the time you spend
  Development of C++ is very slow and error-prone. You may obtain a highly optimized Java program outperforming an equivalent one in C++ with the same time.
  If a program it not computation-intensive (spending most of the time on things other than computation, like disk I/O and network I/O), then the performance of programming languages will play a less important role
  Performance of a programming languages depends on both the interface (language specifications) and the implementation (compiler and libraries)
  Benchmark, benchmark, benchmark!

## Slide 42: Performance of Programming Languages
C/C++ is performant, but how about others?
The performance of Python is insane!!!
  I really don’t like Python. I can discuss this when having a chance
  Why is Python slow?

## Slide 43: Performance of Programming Languages
Just-in-Time compilation (JIT)
C: source code -> native assembly code
Java: two stages
  Compile time: Source code -> Java Bytecode
  Runtime: Java Bytecode is interpreted by Java Virtual Machine (JVM)
    JVM compiles hotspot code into native code to boost performance
    More statistics for optimization, e.g., branch prediction
    James Gosling: Java will be slower if it is compiled ahead of time (AOT)

## Slide 44: Performance of Programming Languages
Is there modern languages with similar performance to C/C++?

## Slide 45: Performance of Programming Languages
Is there modern languages with similar performance to C/C++?
  Rust!
Reasonable languages typically run in no more than 3X time of C on average, including
  JavaScript: Garbage collection, dynamic type
  Go: conservative compiler optimization
    Enough to develop OS
  OCaml: functional language
    Indeed, it is very efficient. No more than 2X of C

## Slide 46: Performance of Programming Languages
It always arouses controversy to compare programming languages…

## Slide 47: After ICS
Two perspectives of learning computer architecture
  User: parallel computing
  Builder: hardware design
Functional programming helps a lot for learning parallel computing
OS knowledge required for understanding multithreading
Network and databases knowledge required to understand distributed computing
Systems courses of PKU are generally too shallow and require too little coding

## Slide 48: Computer Systems Learning Resources: A Recommended List
Written in Jan 2022, still updating
Covering most of the major fields in computer systems
Contains lots of textbooks, courses, online documentations, and abundant guidelines
Latest version website
  https://www.overleaf.com/read/txqjnjxyxqqx
GitHub address
  https://github.com/ZhenbangYou/Computer-Systems-Learning-Resources-A-Recommended-List

## Slide 49: If you want to chat with me …
WeChat
Email: zhenbangyou@pku.edu.cn

## Slide 50: Acknowledgements
My friends (unordered)
  Zirui Ou
  Zeang Sheng
  Yunqi Li
  Yinmin Zhong
  Tingyu Zhu
  Tianchi Li
  All my friends in ICS Seminar 1 in 2021 fall
Course
  Stanford CS149 and its instructors
Books
  Computer Architecture: A Quantitative Approach (6th Edition)