## Slide 1
Cache Memories
Program Optimization
MADE BY: Zhong Zhineng & Song Yixin

## Slide 2
Cache Memories

## Slide 3
Small and fast SRAM memories
Keep frequently accessed blocks of main memory
Cache hit
Cache miss: three types of miss
Cache Memories

## Slide 4
Cache Structure
M, S, E, B, m, s
S cache sets, E cache lines, B blocks
t = m-(b+s) tag bits
Valid bit
C = S×E×B
Address of word: tag + set index + block offset
Bijection from middle s set index bits to S cache sets
Bijection from low b block offset bits to B blocks
2^t address of a cache set => t tag bits

## Slide 5
Cache Structure

## Slide 6
Direct Mapped Cache (E = 1)
  Not match: old line being replaced directly
  Thrash
Associative Cache (1 <E < C/B)
  Not match: one line in the set is selected for eviction and replacement
  Many replacement policies: Random, LRU, LFU, …
Fully Associative Cache (S = 1, E = C/B)
  Search for many matching tags in parallel => expensive and small
  TLB
Cache Classification

## Slide 7
Write hit
  Write-through
  Write-back
Write miss
  Write allocate
  No write allocate
Write through + No write allocate / Write back + Write allocate
Cache Write

## Slide 8
Make use of locality
Make the most frequent the fast
Decrease cache miss within loops
Loop variable orders
Cache Friendly Code

## Slide 9
Cache Mountain

## Slide 10
Program Optimization

## Slide 11
Compiler Optimization
Some can be done by compiler
  Code moving, such as moving the repeating calc inside the loop outside.
  Use shift and add/sub to do mult/div
  Expression reuse
Some cannot be done by compiler (must be conservative)
  Procedure may have side-effects
  Pointer may have aliases

## Slide 12
CPI may be less than 1
In-order issue
Out-of-order execution
In-order commit
Simple Out-of-order Processor

## Slide 13
Out-of-order execution
Multiple issue
Dynamic Scheduling
Speculative execution
Register renaming
Modern CPU

## Slide 14
Critical Path
Critical path: lower bound
Number of function parts
Data passing limitation

## Slide 15
Loop Unrolling: Improve Parallelism

## Slide 16
Separate Accumulators

## Slide 17
Reassociation

## Slide 18
Limitations
Register spilling: k = 20, use stack to store
Floating operation does not have associative law, so changing operation orders may not apply.

## Slide 19
Thanks for listening.